## Slide 1: Pipelining
Prepared By: Aatira Anum

## Slide 2: Fundamental Execution Cycle

## Slide 3: Performance
If one instruction takes 3 nanoseconds to execute the cycle then 3 instructions will take 9 nanoseconds.
5 instructions will take 15 nanoseconds.
10 instructions will take 30 nanoseconds
20 instructions will take 60 nanoseconds.

## Slide 4: How to improve Performance?
Increase Clock Frequency of CPU
Internal clock to synchronize all operations – ensures all circuits inside a computer works together at same time
Clock Cycle Time: Amount of time between 2 adjacent pulses of an oscillator
Single increment of the CPU clock during which the smallest unit of processor activity is carried out
If one instruction cycle takes 3ns then clock cycle time will be of 3ns
Clock Frequency: Number of clock cycles CPU executes per second
Notes: Basic Idea is to reduce execution time

## Slide 5: Clock Frequency
Measured In Hertz.
1 Hertz = 1 clock cycle/second
1 MHz = 106 clock cycles per second
1 GHz = 109 clock cycles per second
Indicator of Processor speed
Notes: Basic Idea is to reduce execution time

## Slide 6: Clock Frequency
What is the clock frequency of the processor if one clock cycle takes 10 ns?
Clock frequency = 1/clock cycle time
= 1/(10 x 10-9)
= 100000000 Hz
= 0.1 GHz
Notes: Basic Idea is to reduce execution time

## Slide 7: Pipelining
Multiple instructions are overlapped in a single execution
It takes advantages of the parallelism that exists among the actions needed to execute an instruction
Key implementation technique to make CPU faster
Notes: Basic Idea is to reduce execution time

## Slide 8: Pipelining
A pipeline is just like an assembly line
In an automobile manufacturing line, there are many steps each contributing something to the construction of the car
Each step operates in parallel with other steps although with a different car
Notes: Basic Idea is to reduce execution time

## Slide 9: Real World Analogy
Automobile manufacturing line without pipelining
Assemble (A), Paint (P), Fix tires (T)
Assuming A+P+T take 3 hours
Time line | 0-3 hours | 3-6 Hours | 6 -9Hours
Car 1 | A+P+T |  | 
Car 2 |  | A+P+T | 
Car 3 |  |  | A+P+T

## Slide 10: Real World Analogy
Automobile manufacturing line with pipelining, in 3 stages
Assemble (A), Paint (P), Fix tires (T)
Assuming each stage takes 1 hour
Time line | 1st hour | 2nd hour | 3rd hour | 4th hour | 5th hour | 6th hour | 7th hour | 8th hour | 9th hour
Car 1 | A | P | T |  |  |  |  |  | 
Car 2 |  | A | P | T |  |  |  |  | 
Car 3 |  |  | A | P | T |  |  |  | 
It takes 5 hours with pipelining and 9hours without pipelining
Speedup = 9/5

## Slide 11: Stages in Execution Cycle
Different architectures divide the execution cycle in different number of stages
E.g., a 3 stage pipeline will be like this
Instruction Fetch
Instruction Decode
Instruction
Execute

## Slide 12: Stages in Execution Cycle
Fetch - Obtain Instruction from Memory
Decode – Determine required action and obtain operands
Execute – Execute the instruction and store the result

## Slide 13: Performance of Pipelined Processor
It takes 3 nanoseconds to execute the whole cycle
Suppose each stage takes 1 nanoseconds
How much time it will take to complete 3 instructions?

## Slide 14: Performance of Pipelined Processor
 | 1 ns | 2ns | 3ns | 4ns | 5ns
1st instruction | F | D | E |  | 
2nd instruction |  | F | D | E | 
3rd instruction |  |  | F | D | E

## Slide 15: Performance of Pipelined Processor
Total time taken to execute 3 instructions in pipelined processor = 5ns
Total time taken to execute 3 instructions in non-pipelined processor = 9ns
Speedup = 9/5 = 1.8

## Slide 16: Latency and Throughput
Latency – time taken to complete an instruction
Non-pipelined = 3ns
Pipelined = 3ns
Throughput – number of instructions executed per unit time
Non-pipelined = 3/9 = 0.3 instructions/ns
Pipelined = 3/5 = 0.6 instructions/ns
Observation : Observation: Pipeline does not improve latency, it only improves throughput

## Slide 17: Performance of Pipelined Processor
Assumption
  All stages take equal time.
It takes 3 nanoseconds to execute the whole cycle
Suppose Fetch stage takes 0.5 nanoseconds, Decode stage takes 2 nanoseconds and Execute stage takes 0.5 nanoseconds.
How much time it will take to complete 3 instructions?

## Slide 18: Performance of Pipelined Processor
1st instruction | 0-0.5 | 0.5-2.5 | 2.5-3 |  | 
2nd instruction |  | 0.5-2.5 | 2.5-4.5 | 4.5-5 | 
3rd instruction |  |  | 2.5-4.5 | 4.5-6.5 | 6.5-7
Fetch stage takes 0.5 nanoseconds,
Decode stage takes 2 nanoseconds
Execute stage takes 0.5 nanoseconds.

## Slide 19: Latency and Throughput
Pipelined with all stages not of equal time
Total time taken = 7ns
Latency = 4.5 ns
Throughput = 3/7 instructions/ns

## Slide 20: Performance of Pipelined Processor
Assumption
  There is no time taken to move from one stage to another.
Pipeline buffers stores the output of each stage.
It takes time for pipeline buffers to operate and this adds to the instruction cycle time.
Latch time/delay is the time taken to transition from one stage to another.
Suppose in the previous example, the latch time is 0.2 nanoseconds, how much time is taken to execute 3 instructions?

## Slide 21: Performance of Pipelined Processor
1st | F |  | D |  | E |  |  |  | 
2nd |  |  | F |  | D |  | E |  | 
3rd |  |  |  |  | F |  | D |  | E
Fetch stage takes 0.5 nanoseconds,
Decode stage takes 2 nanoseconds
Execute stage takes 0.5 nanoseconds.
Latch time is 0.2 nanoseconds.

## Slide 22: Latency and Throughput
Pipelined with all stages not of equal time and latch time
Total time taken = 7 + 0.2 x4 = 7.8 ns
Latency = 4.5 + 0.2 x2 = 4.9 ns
Throughput = 3/7.8 instructions/ns

## Slide 23: Throughput and Latency for 3 instructions
Case | Latency | Throughput | Speed up
Non pipeline | 3 | 3/9=0.33 | NA
Pipeline ideal case | 3 | 3/5=0.6 | 9/5
Pipeline with all stages not of equal time | 4.5 | 3/7=0.42 | 9/7
Non ideal case with latch time | 4.9 | 3/7.8=0.38 | 9/7.8

## Slide 24: Clock Cycle
Internal clock to synchronize all operations – ensures all circuits inside a computer works together at same time
Clock Cycle Time: Single increment of the CPU clock during which the smallest unit of processor activity is carried out
In processor with no pipelining
  If one instruction cycle takes 3ns then clock cycle time should be of 3ns
In ideal pipelining case
  If each stage takes 1 ns
  Clock cyle time should be of 1ns
In pipelining with different stages taking different time
  F takes 0.5 ns, D takes 2 ns E takes 0.5ns
  Clock cyle time should be of 2 ns
  The stage with maximum time will be the time taken for each stage
  Each stage will complete in 1 clock cycle time

## Slide 25: Clock Cycle
Each stage will complete in 1 clock cycle time so the time for each stage will be 2 ns.
1st instruction | 0-2 | 2-4 | 4-6 |  | 
2nd instruction |  | 2-4 | 4-6 | 6-8 | 
3rd instruction |  |  | 4-6 | 6-8 | 8-10

## Slide 26: Latency and Throughput
Total time taken = 10 ns
Latency = 6 ns
Throughput = 3/10 instructions/ns (this is worse than non-pipelined version)
This issue can be resolve if stages are more or less of equal time duration (decode stage can be divided into further stages)

## Slide 27: Pipeline with 5 stages
Fetch instruction (FI): Read the next expected instruction into a buffer.
Decode instruction (DI): Determine the opcode and the operand specifiers.
Fetch operands (FO): Fetch each operand.
Execute instruction (EI): Perform the indicated operation.
Write operand (WO): Store the result in register or memory.

## Slide 28: Pipeline in Computer:: Stages
Five-stage pipeline can reduce the execution time for 3 instructions from 15 clock cycles to 7 clock cycles.
Throughput with pipeline= 3/7
Throughput without pipeline= 3/15
Speedup= 15/7
Instruction 1 | FI | DI | FO | EI | WO |  | 
Instruction 2 |  | FI | DI | FO | EI | WO | 
Instruction 3 |  |  | FI | DI | FO | EI | WO

## Slide 29: Pipeline in Computer:: Performance Ideal case (Derivations)
If
  All stages take equal amount of time T
  Latch time=0
  Stages =k
  Number of instructions = n
Then
  Clock cycle of pipeline=T, clock cycle of non pipeline= k*T
  Frequency of pipeline=1/T , Frequency of non pipeline=1/k*T
  Time taken to complete n instructions without pipeline= n*k*T= n*clock cycle of non pipeline
  Through put for n instructions without pipeline= n/ n*k*T
  Time taken to complete n instructions with pipeline= (k+n-1)*T= (k+n-1)*(Clock Cycle of pipeline)
  Through put for n instructions with pipeline= n/ (k+n-1)*T
  Speedup for n instructions = n*k*T/ (k+n-1)*T = n*k/ (k+n-1)
  Latency without pipelining = k*T
  Latency with pipelining= k*T

## Slide 30: Pipeline in Computer:: Performance Non Ideal case (Derivations)
If all stages do not take same time
  Non pipeline processor takes T1 time to complete one instruction
  In pipeline processor max time take by any stage is T2
  Latch time=0
  Stages =k
  Number of instructions = n
Then
  Clock cycle of pipeline processor = T2, Clock Cycle of processor without pipelining = T1
  Frequency of pipeline processor =1/T2, Frequency of processor without pipelining = 1/T1
  Time taken to complete n instructions without pipeline= n*T1= n*clock cycle of non pipeline
  Through put for n instructions without pipeline= n/ n*T1
  Time taken to complete n instructions with pipeline= (k+n-1)*T2 =(k+n-1)*(Clock Cycle of pipeline)
  Through put for n instructions with pipeline= n/ (k+n-1)*T2
  Speedup for n instructions = n*T1/ (k+n-1)*T2
  Latency without pipelining = T1
  Latency with pipelining= K*T2

## Slide 31: Pipeline in Computer:: Performance Non Ideal case with latch time (Derivations)
If all stages do not take same time
  Non pipeline processor takes T1 time to complete one instruction
  In pipeline processor max time take by any stage is T2
  Latch time=T3
  Stages =k
  Number of instructions = n
Then
  Clock cycle of pipeline processor = T2+T3, Clock Cycle of processor without pipelining = T1
  Frequency of pipeline processor =1/(T2+T3), Frequency of processor without pipelining = 1/(T1)
  Time taken to complete n instructions without pipeline= n*T1= n*clock cycle of non pipeline
  Through put for n instructions without pipeline= n/ n*T1
  Time taken to complete n instructions with pipeline= (k+n-1)*(T2+T3)= (k+n-1)*(Clock Cycle of pipeline)
  Through put for n instructions with pipeline= n/ (k+n-1)*(T2+T3)
  Speedup for n instructions = n*T1/ (k+n-1)*(T2+T3)
  Latency without pipelining = T1
  Latency with pipelining= K*(T2+T3)