## Slide 1: Cache Memory
By: Aatira Anum

## Slide 2: Memory Organization
Processor
Registers
Memory
(RAM)
Hard Drive

## Slide 3: Key Characteristics of Computer Memory Systems
Location
  Internal
  External
Capacity
  No of Words/Bytes
Unit of Transfer
  Word
  Block
Performance
  Access Time

## Slide 4: Memory Organization
Registers
  Temporary Storage inside processor
  Very Fast
  Very expensive
  Small capacity/size
Main Memory
  Random access memory
  Internal Memory
  Normal fast
  Affordable
  Medium Capacity
  Temporary Storage
Hard Drive
  Slow
  Cheap
  Large Size/capacity
  Permanent Storage

## Slide 5: Main Memory Latency is Long
2.0 GHz CPU 0.5 ns cycle time
100 ns memory 200 cc memory latency
Solution: Caches

## Slide 6: Caches
More closer to processor than main memory
Very Fast and Very Expensive
Smaller size and capacity
Registers
Cache
Main Memory
External Hard Dive
Memory Hierarchy

## Slide 7: Cache Memory Principles
The cache contains a copy of portions of main memory.
When the processor attempts to read a word of memory, a check is made to determine if the word is in the cache.
If so, the word is delivered to the processor.
If not, a block of main memory, consisting of some fixed number of words, is read into the cache and then the word is delivered to the processor.
When a block of data is fetched into the cache to satisfy a single memory reference, it is likely that there will be future references to that same memory location or to other words in the block.

## Slide 8: Cache Memory Principles
Cache hit
  copy is in cache, quick access
Cache miss
  copy not in cache, read address and possibly its neighbors into cache

## Slide 9: Levels of Cache

## Slide 10: Average Access Time
Suppose it requires 100 ns to access memory
Suppose the processor has two-level of cache memory
It requires 10 ns to access level 1 cache and 90% of memory accesses are found in cache level 1
It requires 30 ns to access level 2 cache and 10% of memory accesses are found in cache level 2
What is the average time to access a location?
Average Access Time = 0.9(10) + 0.1(10 + 30) = 13 ns

## Slide 11: Cache Structure
Index: A number to each block/cell of cache
Tag: Used to keep complete or part of address of data the was brought from main memory
Data: To keep data brought from RAM
Value Bit: A single bit use to show if the data is updated after bringing it in from RAM
Index | Tag | Data | Value Bit
0 |  |  | 
1 |  |  | 
2 |  |  | 
N |  |  | 

## Slide 12: Cache Size
Small enough so that the overall average cost per bit is close to that of main memory alone
Large enough so that the overall average access time is close to that of the cache alone
The larger the cache, the larger the number of gates involved in addressing the cache. The result is that large caches tend to be slightly slower than small ones—even when built with the same integrated circuit technology and put in the same place on chip and circuit board.
The available chip and board area also limits cache size. Because the performance of the cache is very sensitive to the nature of the workload, it is impossible to arrive at a single “optimum” cache size.

## Slide 13: Mapping Function
Because there are fewer cache lines than main memory blocks, an algorithm is needed for mapping main memory blocks into cache lines. Further, a means is needed for determining which main memory block currently occupies a cache line.
The choice of the mapping function dictates how the cache is organized. Three techniques can be used:
  Direct
  Associative
  Set-associative

## Slide 14: Associative Mapping
Any cell of main memory can be loaded in any cell of Cache
Addresses of RAM are stored as Tag
The cache control logic must simultaneously examine every tag for a match
Pros:
  Flexibility
Cons:
  Larger value of tag
  Number of bits required for tag= log2(size of RAM)
    For 1MB RAM tag size is of 20 bits

## Slide 15
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
Cache
Main Memory
Addresses to access in memory:
0000, 0011, 1000, 1010, 1110, 0000, 0000

## Slide 16
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
Cache
Main Memory
Read 0000
It’s a miss
Addresses to access in memory:
0000, 0011, 1000, 1010, 1110, 0000, 0000

## Slide 17
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 0000 | A | 0
1 |  |  | 
2 |  |  | 
3 |  |  | 
Cache
Main Memory
Bring 0000 to Cache
Addresses to access in memory:
0000, 0011, 1000, 1010, 1110, 0000, 0000

## Slide 18
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 0000 | A | 0
1 |  |  | 
2 |  |  | 
3 |  |  | 
Cache
Main Memory
Read 0011
It’s a miss
Addresses to access in memory:
0000, 0011, 1000, 1010, 1110, 0000,0000

## Slide 19
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 0000 | A | 0
1 | 0011 | D | 0
2 |  |  | 
3 |  |  | 
Cache
Main Memory
Bring 0011 to cache
Addresses to access in memory:
0000, 0011, 1000, 1010, 1110, 0000, 0000

## Slide 20
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 0000 | A | 0
1 | 0011 | D | 0
2 | 1000 | I | 0
3 |  |  | 
Cache
Main Memory
Read 1000
It’s a miss
Addresses to access in memory:
0000, 0011, 1000, 1010, 1110, 0000, 0000

## Slide 21
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 0000 | A | 0
1 | 0011 | D | 0
2 | 1000 | I | 0
3 | 1010 | K | 0
Cache
Main Memory
Read 1010. It’s a miss. Bring 1010 to cache
Addresses to access in memory:
0000, 0011, 1000, 1010, 1110, 0000, 0000

## Slide 22
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 0000 | A | 0
1 | 0011 | D | 0
2 | 1000 | I | 0
3 | 1010 | K | 0
Cache
Main Memory
Read 1110
It’s a miss, there is no space.
Addresses to access in memory:
0000, 0011, 1000, 1010, 1110, 0000,0000

## Slide 23: Replacement Algorithms
Once the cache has been filled, when a new block is brought into the cache, one of the existing blocks must be replaced.

## Slide 24: Replacement Algorithm (LRU)
Probably the most effective is least recently used (LRU):
  Replace that block in the set that has been in the cache longest with no reference to it.
LRU is also relatively easy to implement for a fully associative cache.
  The cache mechanism maintains a separate list of indexes to all the lines in the cache.
  When a line is referenced, it moves to the front of the list.
  For replacement, the line at the back of the list is used.
Because of its simplicity of implementation, LRU is the most popular replacement algorithm.

## Slide 25: Other Replacement Policies
First-in-first-out (FIFO):
  Replace that block in the set that has been in the cache longest.
  FIFO is easily implemented as a round-robin or circular buffer technique.
Least frequently used (LFU):
  Replace that block in the set that has experienced the fewest references.
  LFU could be implemented by associating a counter with each line.
Random Replacement
  Pick a line at random from among the candidate lines.

## Slide 26
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 0000 | A | 0
1 | 0011 | D | 0
2 | 1000 | I | 0
3 | 1010 | K | 0
Cache
Main Memory
Read 1110
It’s a miss, there is no space.
Addresses to access in memory:
0000, 0011, 1000, 1010, 1110, 0000,0000

## Slide 27
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 1110 | O | 0
1 | 0011 | D | 0
2 | 1000 | I | 0
3 | 1010 | K | 0
Cache
Main Memory
Bring 1110 in place of least recently used, which is 0000
Addresses to access in memory:
0000, 0011, 1000, 1010, 1110, 0000, 0000

## Slide 28
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Cache
Main Memory
Read 0000
It’s a miss
Cache is full so we replace the least recently used element (i.e 0011),
Index | Tag | Data | Value Bit
0 | 1110 | O | 0
1 | 0011 | D | 0
2 | 1000 | I | 0
3 | 1010 | K | 0
Addresses to access in memory:
0000, 0011, 1000, 1010, 1110, 0000, 0000

## Slide 29
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Cache
Main Memory
Bring 0000 in cache by replacing 0011
Note the now 0000 is on index 1
Index | Tag | Data | Value Bit
0 | 1110 | O | 0
1 | 0000 | A | 0
2 | 1000 | I | 0
3 | 1010 | K | 0
Addresses to access in memory:
0000, 0011, 1000, 1010, 1110, 0000,0000

## Slide 30
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 1110 | O | 0
1 | 0000 | A | 0
2 | 1000 | I | 0
3 | 1010 | K | 0
Cache
Main Memory
Read 0000
It’s a hit
Addresses to access in memory:
0000, 0011, 1000, 1010, 1110, 0000,0000

## Slide 31: Hit and Miss Rate
0000, 0011, 1000, 1010, 1110, 0000,0000
Hit rate = 1/7
Miss rate = 6/7

## Slide 32: Direct Mapping
Main Memory address is dived into 2 fields
  Index = Main Memory Address% Size of Cache
    Data is placed in cache at this index
  Tag= Main Memory Address / Size of Cache
    As stored in cache along with data
  Main Memory Address= Tag*Size of Cache + Index

## Slide 33: Direct Mapping
The size of tag will depend of size of cache and size of RAM
  Number of bits required for tag= log2(size of Ram/ Size of Cache)
  Number of bits required for index= log2(size of cache)
Tip:
  Tagb:Indexb= Main Memory Address b

## Slide 34: Direct Mapping
Question:
  If cache is of 8 words and Ram of 16 words
    What is the size of tag?
If cache is of 8 words and Ram of 16 words
    What is the size of tag?
    Answer log2(16/8)= 1

## Slide 35: Direct Mapping
Question:
  If cache is of 1k Words and Ram is of 1M words
    What is the size of tag?
If cache is of 1k Words and Ram is of 1M words
    What is the size of tag?
    Answer = log 2(2^20/2^10)= 10

## Slide 36
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
Cache
Main Memory
Addresses to access in memory:
0000, 0100, 1001

## Slide 37
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
Cache
Main Memory
Read 0000
The tag and index of this address is
Tag=00b Index=00b
It’s a miss
Addresses to access in memory:
0000, 0100, 1001
  Index = Main Memory Address% Size of Cache
  Tag= Main Memory Address / Size of Cache

## Slide 38
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 00 | A | 0
1 |  |  | 
2 |  |  | 
3 |  |  | 
Cache
Main Memory
0000b will be placed on cache at index 00 and tag 00 will be stored
Addresses to access in memory:
0000, 0100, 1001
  Index = Main Memory Address% Size of Cache
  Tag= Main Memory Address / Size of Cache

## Slide 39
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 00 | A | 0
1 |  |  | 
2 |  |  | 
3 |  |  | 
Cache
Main Memory
Read 0100b (4d)
The tag and index of this address is
Tag=01b Index=00b
It’s a miss
Addresses to access in memory:
0000, 0100, 1001
  Index = Main Memory Address% Size of Cache
  Tag= Main Memory Address / Size of Cache

## Slide 40
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 01 | E | 0
1 |  |  | 
2 |  |  | 
3 |  |  | 
Cache
Main Memory
0100b (4d) will be placed on cache at index 00 and tag 01 will be stored
But index 00 already has some data, we will replace that
Note that even rest of the cache is free 0100 will go at index 00b
Addresses to access in memory:
0000, 0100, 1001
  Index = Main Memory Address% Size of Cache
  Tag= Main Memory Address / Size of Cache

## Slide 41
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 01 | E | 0
1 |  |  | 
2 |  |  | 
3 |  |  | 
Cache
Main Memory
Read 1001 (9d)
The tag and index of this address is
Tag=10b Index=01b
It’s a miss
Addresses to access in memory:
0000, 0100, 1001
  Index = Main Memory Address% Size of Cache
  Tag= Main Memory Address / Size of Cache

## Slide 42
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 01 | E | 0
1 | 10 | J | 0
2 |  |  | 
3 |  |  | 
Cache
Main Memory
1001 will be placed on cache at index 01 and tag 10 will be stored
Addresses to access in memory:
0000, 0100, 1001
  Index = Main Memory Address% Size of Cache
  Tag= Main Memory Address / Size of Cache

## Slide 43
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 00 | A | 0
1 | 10 | J | 0
2 | 11 | ? | 0
3 |  |  | 
Cache
Main Memory
Question:
See the tag at index 2 of cache. What data is placed over there?
  Index = Main Memory Address% Size of Cache
  Tag= Main Memory Address / Size of Cache
  Main Memory Address= Tag*Size of Cache + Index

## Slide 44
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit
0 | 00 | A | 0
1 | 10 | J | 0
2 | 11 | O | 0
3 |  |  | 
Cache
Main Memory
Question:
See the tag at index 2 of cache. What data is placed over there?
Answer: O ie data of address 1110
  Index = Main Memory Address% Size of Cache
  Tag= Main Memory Address / Size of Cache

## Slide 45: Set Associative Mapping
In direct Mapping two words with same index but different tags cannot reside in cache at same time
  For figure given in slide 39, data of address 0000 and 0100 cannot reside in cache at same time
In set associative mapping there are multiple sets and words with same index but different tags can reside in cache at same time
If there are k sets then k elements with same index can reside in cache
All the sets are checked simultaneously to see if the data is in cache

## Slide 46
set 0 set 1

## Slide 47
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit | Tag | Data | Value Bit
0 |  |  |  |  |  | 
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
Cache
Main Memory
set 0 set 1

## Slide 48
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit | Tag | Data | Value Bit
0 |  |  |  |  |  | 
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
Cache
Main Memory
set 0 set 1
Read 0000
Tag= 00 index =00
It’s a miss

## Slide 49
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit | Tag | Data | Value Bit
0 | 00 | A | 0 |  |  | 
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
Cache
Main Memory
set 0 set 1
0000 will be placed it in index 00 and tag will be equal to 00
We place it in set 0 because it was empty slot

## Slide 50
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit | Tag | Data | Value Bit
0 | 00 | A | 0 | 01 | E | 0
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
Cache
Main Memory
set 0 set 1
Read 0100
Tag= 01 index =00
It’s a miss

## Slide 51
Address | Word
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | I
1001 | J
1010 | K
1011 | L
1100 | M
1101 | N
1110 | O
1111 | P
Index | Tag | Data | Value Bit | Tag | Data | Value Bit
0 | 00 | A | 0 | 01 | E | 0
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
Cache
Main Memory
set 0 set 1
0100 will be placed it in index 00 and tag will be 01
We place it in set 1 because it was empty slot

## Slide 52: Write Policy
When a block that is resident in the cache is to be replaced, there are two cases to consider.
  If the old block in the cache has not been altered, then it may be overwritten with a new block without first writing out the old block.
  If at least one write operation has been performed on a word in that line of the cache, then main memory must be updated by writing the line of cache out to the block of memory before bringing in the new block.

## Slide 53: Writing Policy
The simplest technique is called write through.
  Using this technique, all write operations are made to main memory as well as to the cache, ensuring that main memory is always valid.
  Disadvantage of this technique is that it generates substantial memory traffic and may create a bottleneck.
An alternative technique, known as write back, minimizes memory writes.
  With write back, updates are made only in the cache.
  When an update occurs, a dirty bit, or value bit, associated with the line is set.
  When a block is replaced, it is written back to main memory if and only if the dirty bit is set.
  The problem with write back is that portions of main memory are invalid, and hence accesses by I/O modules can be allowed only through the cache.