## Slide 1: Pipeline II
Hazards

## Slide 2: Pipeline with 5 stages
Fetch instruction (FI): Read the next expected instruction into a buffer.
Decode instruction (DI): Determine the opcode and the operand specifiers.
Fetch operands (FO): Fetch each operand.
Execute instruction (EI): Perform the indicated operation.
Write operand (WO): Store the result in register or memory.

## Slide 3: Pipeline with 5 stages
 | 1st | 2nd | 3rd | 4th | 5th | 6th | 7th
add ax, bx | FI | DI | FO | EI | WO |  | 
add cx, dx |  | FI | DI | FO | EI | WO | 
sub si, di |  |  | FI | DI | FO | EI | WO

## Slide 4: Pipeline Hazard in Computer
Problems with the instruction pipeline in CPU when the next instruction cannot execute in the following clock cycle and can potentially lead to incorrect computation results.
Three Hazard types:
  Structural/Resource
    same resource is needed multiple times in the same cycle
  Data
    Instruction depends on result of prior instruction still in the pipeline data dependencies limit pipelining
  Control
    Next executed instruction may not be the next specified instruction

## Slide 5: Structural/Resource Hazard
A resource hazard occurs when two (or more) instructions that are already in the pipeline need the same resource.
The result is that the instructions must be executed in serial rather than parallel for a portion of the pipeline.
Examples:
  Two accesses to a single ported memory
Solutions:
  Increase available resources
  Stalling

## Slide 6: Structural/Resource Hazard
add ax, [num1] | FI | DI | FO | EI | WO |  | 
add cx, dx |  | FI | DI | FO | EI | WO | 
sub ax, dx |  |  | FI | DI | FO | EI | WO
Assume we have a Single Port Memory

## Slide 7: Structural/Resource Hazard
add ax, [num1] | FI | DI | FO | EI | WO |  |  | 
add cx, dx |  | FI | DI | FO | EI | WO |  | 
sub ax, dx |  |  | Stall | FI | DI | FO | EI | WO
Solution
Stall - Waste one clock cycle

## Slide 8: Data Hazards
Data hazards occur when instructions that exhibit data dependence modify data in different stages of a pipeline.
Three types of data hazards
  RAW: Read after Write or Flow dependency
  WAR: Write after Read or anti-dependency
  WAW: Write after Write or Output dependency

## Slide 9: Data Hazards
RAW: Read after Write or Flow dependency
  add ax, cx
  add bx, ax
WAW: Write after Write or output dependency
  add ax, bx
  add ax, cx
WAR: Write after Read or anti-dependency
  add ax, bx
  add bx, cx

## Slide 10: Read after Write (RAW) or flow dependency
Next Instruction tries to read operand before first Instruction writes it
add ax, bx | FI | DI | FO | EI | WO |  | 
add cx, ax |  | FI | DI | FO | EI | WO | 

## Slide 11: Read after Write (RAW) or flow dependency
Solution 1 Stalling – waste two clock cycles and fetch operand after WO stage of 1st instruction
add ax, bx | FI | DI | FO | EI | WO |  |  | 
add cx, ax |  | FI | DI | Stall | Stall | FO | EI | WO

## Slide 12: Read after Write (RAW) or flow dependency
Solution 2 Data Forwarding
    Used in RAW dependency, data is forwarded to next instruction as soon as its available so that next instruction doesn’t have to wait for write operand
    Needs changes in hardware
    Needs only one stall
add ax, bx | FI | DI | FO | EI | WO |  | 
add cx, ax |  | FI | DI | Stall | FO | EI | WO

## Slide 13: Write after write (WAW), or output dependency
Two instructions both write to the same location.
A hazard occurs if the write operations take place in the reverse order of the intended sequence.
    I: write to location X
    J: write to location X
  Incorrect answer if J finishes before I
Can not occur in this pipeline

## Slide 14: Write after read (WAR) or antidependency
An instruction reads a register or memory location and a succeeding instruction writes to the location.
A hazard occurs if the write operation completes before the read operation takes place.
    I: read from location X
    J: write to location X
  Incorrect answer if J finishes before I
Can not occur in this pipeline

## Slide 15: Control Hazard
A control hazard, also known as a branch hazard
Occurs when the pipeline makes the wrong decision on a branch prediction and therefore brings instructions into the pipeline that must subsequently be discarded

## Slide 16: Control Hazard
Instruction 1
Instruction 2 (Conditional Branch Instruction to label1)
Instruction 3
Instruction 4
Instruction 5
label1: Instruction 6
Assuming no RAW or structural hazard.

## Slide 17
 | 1
Instruction 1 | FI
Branch Instruction | 
Instruction 3 | 
Instruction 4 | 
Instruction 5 | 
label1: Instruction 6 | 

## Slide 18
Instruction 2 is conditional branching
 | 1 | 2
Instruction 1 | FI | DI
Branch Instruction |  | FI
Instruction 3 |  | 
Instruction 4 |  | 
Instruction 5 |  | 
label1: Instruction 6 |  | 

## Slide 19
Until the instruction is actually executed, it is impossible to determine whether the branch will be taken or not.
 | 1 | 2 | 3
Instruction 1 | FI | DI | FO
Branch Instruction |  | FI | DI
Instruction 3 |  |  | ?
Instruction 4 |  |  | 
Instruction 5 |  |  | 
label1: Instruction 6 |  |  | 

## Slide 20: Dealing with Branches
How to handle Branches? Solution: Branch Prediction
Branch Prediction Strategies:
Always Untaken i.e. fetch next instruction
Always Taken i.e. fetch instruction whose offset is in the instruction
Delayed Branch i.e. add some code between branch instruction and target instruction
Dynamic Prediction on the basis of history of a branch

## Slide 21: Dealing with Branches
How to handle Branches? Solution: Branch Prediction
Branch Prediction Strategies:
Always Untaken i.e. fetch next instruction
Always Taken i.e. fetch instruction whose offset is in the instruction
Delayed Branch i.e. add some code between branch instruction and target instruction
Dynamic Prediction on the basis of history of a branch

## Slide 22
Processor predicts that the branch is not taken and fetch next instruction.
 | 1 | 2 | 3
Instruction 1 | FI | DI | FO
Branch Instruction |  | FI | DI
Instruction 3 |  |  | FI
Instruction 4 |  |  | 
Instruction 5 |  |  | 
label1: Instruction 6 |  |  | 

## Slide 23
What if branch prediction is wrong?
All work from Instruction 3-5 is wasted.
 | 1 | 2 | 3 | 4 | 5
Instruction 1 | FI | DI | FO | EI | WO
Branch Instruction |  | FI | DI | FO | EI
Instruction 3 |  |  | FI | DI | FO
Instruction 4 |  |  |  | FI | DI
Instruction 5 |  |  |  |  | FI
label1: Instruction 6 |  |  |  |  | 

## Slide 24
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Instruction 1 | FI | DI | FO | EI | WO |  |  |  |  | 
Branch Instruction |  | FI | DI | FO | EI | WO |  |  |  | 
Instruction 3 |  |  | FI | DI | FO |  |  |  |  | 
Instruction 4 |  |  |  | FI | DI |  |  |  |  | 
Instruction 5 |  |  |  |  | FI |  |  |  |  | 
label1: Instruction 6 |  |  |  |  |  | FI | DI | FO | EI | WO
How many cycles are wasted?

## Slide 25: Control Hazard
A control hazard, also known as a branch hazard
Occurs when the pipeline makes the wrong decision on a branch prediction and therefore brings instructions into the pipeline that must subsequently be discarded

## Slide 26: Summary: Pipelining Hazards
Resource/Structural Hazard
  Add more resource
  Stall
Data Hazards
  Stall
  Data Forwarding
Control Hazard
  Stall