## Slide 1: Decoders
Reference: Chapter 3
Moris Mano 4th Edition

## Slide 2: Minterms
Total Variables = 3
All Possible Minterms/Combinations/Product Terms = 2^3 = 8

## Slide 3: Minterm0
X
Y
Z
m0 = X’Y’Z’
0
0
0
1
1
1
1
Test m0 on (000)2 = (0)10
Output = 1

## Slide 4: Minterm0
X
Y
Z
m0 = X’Y’Z’
0
0
1
0
1
1
0
Test m0 on (001)2 = (1)10
Output = 0

## Slide 5: Minterm0
X
Y
Z
m0 = X’Y’Z’
0
0
1
0
1
1
0
Test m0 on (001)2 = (1)10
Conclusion:
mi gives output 1 only on binary equivalent of (i)10
For other combinations, output is 0.

## Slide 6: Combining all Minterms of 3 Variables
= m0
= m1
= m2
= m3
= m4
= m5
= m6
= m7
Circuit containing all the minterms of 3 variables

## Slide 7: Combining all Minterms of 3 Variables
= m0
= m1
= m2
= m3
= m4
= m5
= m6
= m7
Circuit containing all the minterms of 3 variables
Which output signal will be ON on input (110)2?
0
1
1

## Slide 8: Combining all Minterms of 3 Variables
= m0
= m1
= m2
= m3
= m4
= m5
= m6
= m7
Circuit containing all the minterms of 3 variables
1

## Slide 9: Combining all Minterms of 3 Variables
= m0
= m1
= m2
= m3
= m4
= m5
= m6
= m7
Circuit containing all the minterms of 3 variables
What will be the behavior of other output signals?
1
0
1
1

## Slide 10: Combining all Minterms of 3 Variables
= m0
= m1
= m2
= m3
= m4
= m5
= m6
= m7
Circuit containing all the minterms of 3 variables
1
0
0
0
0
0
0
0

## Slide 11: How Minterms Work?
Input |  |  | Output |  |  |  |  |  |  | 
X | Y | Z | m0 X’Y’Z’ | m1 X’Y’Z | m2 X’YZ’ | m3 X’YZ | m4 XY’Z’ | m5 XY’Z | m6 XYZ’ | m7 XYZ
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Truth Table of circuit generating all minterms

## Slide 12: Circuit to generate all Minterms
= m0
= m1
= m2
= m3
= m4
= m5
= m6
= m7
This is called Decoder

## Slide 13: Decoder
A0
…
An-1
D0
D1
D2
Dm-1
.
.
.
n to 2n
Decoder
m = 2n
Objective:
Take n inputs
Generate 2n minterms (i.e. all possible product terms)
OR
Take input signal = (i)10
Generate signal 1 at Di and 0 at rest of the outputs
n inputs
2n Minterms
- Only 1 minterm will be 1 at a time, rest will be 0
- Di will be 1 for its corresponding combination

## Slide 14: Decoder…
1 | 1 | 1 | 0
Input
?
4-to-16
Decoder

## Slide 15: Decoder…
1 | 1 | 1 | 0
Input
4-to-16
Decoder
(1110)2 = (14)10
Output
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 16: Decoder…
1 | 1 | 1 | 0
Input
4-to-16
Decoder
(1110)2 = (14)10
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Output

## Slide 17: 1-to-2 Line Decoder
Input | Output | 
A | D0 | D1
0 | 1 | 0
1 | 0 | 1
1×2
Decoder
A
D0
D1
Decoder Block
(High level Diagram)
D0 = A’ (i.e. m0)
D1 = A (i.e. m1)
(Minterms)
Detailed Logic Diagram
We need equation
for every output
wire

## Slide 18: 2-to-4 Line Decoder
Input |  | Output |  |  | 
A1 | A0 | D0 | D1 | D2 | D3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
2×4
Decoder
A1
D2
D3
Decoder Block
D0 = A1’A0’
D1 = A1’A0
D2 = A1A0’
D3 = A1A0
(All possible Minterms)
Detailed Logic Diagram
D0
D1
A0

## Slide 19: 3-to-8 Line Decoder

## Slide 20: Decoder with Enable Input

## Slide 21: Decoder with Enable Input
Input |  |  | Output |  |  | 
EN | A1 | A0 | D0 | D1 | D2 | D3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
2-to-4 Line Decoder with Enable Input
Decoder Outputs
Enabling Circuit
Application: MagicBulb with Secret Switch

## Slide 22: Decoder with Enable Input
Input |  |  | Output |  |  | 
EN | A1 | A0 | D0 | D1 | D2 | D3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
2-to-4 Line Decoder with Enable Input
Decoder Outputs
Enabling Circuit
Application: MagicBulb with Secret Switch
0
0
0
0
0

## Slide 23: Decoder with Enable Input
Input |  |  | Output |  |  | 
EN | A1 | A0 | D0 | D1 | D2 | D3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
2-to-4 Line Decoder with Enable Input
Decoder Outputs
Enabling Circuit
Application: MagicBulb with Secret Switch
0
0
0
0
0
0
0
0
0
0 . X = 0

## Slide 24: Decoder with Enable Input
Input |  |  | Output |  |  | 
EN | A1 | A0 | D0 | D1 | D2 | D3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
2-to-4 Line Decoder with Enable Input
Decoder Outputs
Enabling Circuit
Application: MagicBulb with Secret Switch
1
1 . X = X

## Slide 25: Implementing Functions using Decoder

## Slide 26: Decoder-Based Combinational Circuit
Example: Decoder and OR-Gate Implementation of 1-Bit Binary Adder
Input |  |  | Output | 
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Truth Table for 1-bit Binary Adder
S(X,Y,Z) = ∑m(1,2,4,7)
C(X,Y,Z) = ∑m(3,5,6,7)

## Slide 27: Decoder-Based Combinational Circuit
Example: Decoder and OR-Gate Implementation of 1-Bit Binary Adder
Input |  |  | Output | 
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Truth Table for 1-bit Binary Adder
S(X,Y,Z) = ∑m(1,2,4,7)
C(X,Y,Z) = ∑m(3,5,6,7)
Logic Diagram
Test circuit on any combination.

## Slide 28: Decoder-Based Combinational Circuit
Example: Decoder and OR-Gate Implementation of 1-Bit Binary Adder
Input |  |  | Output | 
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Truth Table for 1-bit Binary Adder
S(X,Y,Z) = ∑m(1,2,4,7)
C(X,Y,Z) = ∑m(3,5,6,7)
Logic Diagram
Test circuit on any combination.
0
0
0
1
0
0

## Slide 29: Decoder-Based Combinational Circuit
Example: Decoder and OR-Gate Implementation of 1-Bit Binary Adder
Input |  |  | Output | 
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Truth Table for 1-bit Binary Adder
S(X,Y,Z) = ∑m(1,2,4,7)
C(X,Y,Z) = ∑m(3,5,6,7)
Logic Diagram
Test circuit on any combination.
0
1
1
1
0
1

## Slide 30: Decoder-Based Combinational Circuit
Example: Decoder and OR-Gate Implementation of 1-Bit Binary Adder
Input |  |  | Output | 
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Truth Table for 1-bit Binary Adder
S(X,Y,Z) = ∑m(1,2,4,7)
C(X,Y,Z) = ∑m(3,5,6,7)
Logic Diagram
Test circuit on any combination.
1
1
1
1
1
1

## Slide 31: Decoder-Based Combinational Circuit
To implement a function with n inputs and m outputs using Decoder and OR gates we need
An n x 2^n Line Decoder
m OR Gates

## Slide 32: Encoder
A Digital function that performs inverse of a Decoder
m-to-n
Encoder
(m = 2n)
.
.
.
I0
I1
I2
Im
Y0
Y1
Yn

## Slide 33: Octal to Binary Encoder
Functionality:
Take an octal digit
Produce its Binary Equivalent
Octal-to-Binary
Encoder
.
.
.
D0
D1
D2
D7
A0
A1
A2

## Slide 34: Octal to Binary Encoder
Assumption: Only 1 input has value = 1 at any given time.
Can you write equations for A0, A1 and A2?

## Slide 35: Octal to Binary Encoder
A0 = D1 + D3 + D5 + D7
A1 = D2 + D3 + D6 + D7
A2 = D4 + D5 + D6 + D7
Can you make circuit for this Octal to Binary Encoder?

## Slide 36: Limitations of Encoder
Only 1 input should be one at a time otherwise answer will be wrong
E.g. if D3 = D6 = 1
A0 = D1 + D3 + D5 + D7 = 0+1+0+0 = 1
A1 = D2 + D3 + D6 + D7 = 0+1+1+0 = 1
A2 = D4 + D5 + D6 + D7 = 0+0+1+0 = 1
i.e. Encoder Output = (A2A1A0) = (111)2 = (7)8
Which is neither 3 nor 6
Solution: If D3 and D6 both are 1 at the same time, give priority to D6 and output (110)2  Priority Encoder

## Slide 37: Priority Encoder
Truth Table for 4-input Priority Encoder

## Slide 38: Priority Encoder

## Slide 39: Priority Encoder
Logic Diagram of 4-Bit Priority Encoder

## Slide 40: 3-to-8 Line Decoder (Two-Level Implementation)

## Slide 41: 3-to-8 Line Decoder (Hierarchical Design)
Z
Y
X

## Slide 42: 3-to-8 Line Decoder (Hierarchical Design)
Z
Y
X
Z’
Z
Y’
Y
X’
X

## Slide 43: 3-to-8 Line Decoder (Hierarchical Design)
Z
Y
X
Z’
Z
Y’
Y
X’
X
Y’Z’
Y’Z
YZ’
YZ

## Slide 44: 3-to-8 Line Decoder (Hierarchical Design)
Z
Y
X
Z’
Z
Y’
Y
X’
X
Y’Z’
Y’Z
YZ’
YZ
X’Y’Z’
X’Y’Z
X’YZ’
X’YZ
XY’Z’
XY’Z
XYZ’
XYZ

## Slide 45: 6 x 64 Decoder (Non-Hierarchical Design)
A0
A1
A2
A3
A4
A5
.
.
.
.
.
.
.
.
.
.
D0
D1
D2
D63
D62
D61
Level 1
Inverters
Level 2 … ANDs

## Slide 46: 6-to-64 Decoder (Hierarchical Design)

## Slide 47: Two-Level Implementation vs Hierarchical Design

## Slide 48: Gate Input Cost
Gate Input Cost = I + ∑ m × n
I = Total No. of inverters
m = Total gates each with n input

## Slide 49: 3-to-8 Line Decoder (Hierarchical Design)
Gate Input Cost = ?
I = 3
m = 8+4 = 12 ANDs
n = 2 (2 inputs per gate)
Gate Input Cost =
3 + (12 × 2)
= 27

## Slide 50: 6 x 64 Decoder (Non-Hierarchical Design)
A0
A1
A2
A3
A4
A5
.
.
.
.
.
.
.
.
.
.
D0
D1
D2
D63
D62
D61
Gate Input Cost = ?
I = 6
m = 64
n = 6 (Each gate with 6 Inputs)
Gate Input Cost =
I + (n x m)
= 6 + (64 x 6) = 390
Level 1
Inverters
Level 2 … ANDs

## Slide 51: 6-to-64 Decoder (Hierarchical Design)
Gate Input Cost
I = 6
Total AND Gates:
m = 64 + 2x8 +
2x4 = 88
n = 2 (Each AND
gate with 2
inputs)
Gate Input Cost=
I + (n x m)
= 6 + (2x88)
= 182
390 vs 182
Which design is better?

## Slide 52: Constructing 4x16 Decoder using 2x4 Decoders Only
4x16
Decoder
A0
A1
A2
A3
D0
D2
D4
D6
D1
D3
D5
D7
D8
D10
D12
D14
D9
D11
D13
D15

## Slide 53: Constructing 4x16 Decoder using 2x4 Decoders Only
A0
A1
A2
A3
D0
D2
D4
D6
D1
D3
D5
D7
D8
D10
D12
D14
D9
D11
D13
D15
D0
D2
D1
D3
D0
D2
D1
D3
A0
A1
E
A0
A1
E
D0
D2
D1
D3
A0
A1
E
D0
D2
D1
D3
A0
A1
E
1
1
1
1

## Slide 54: Constructing 4x16 Decoder using 2x4 Decoders Only
A0
A1
A2
A3
D0
D2
D4
D6
D1
D3
D5
D7
D8
D10
D12
D14
D9
D11
D13
D15
D0
D2
D1
D3
D0
D2
D1
D3
A0
A1
E
A0
A1
E
D0
D2
D1
D3
A0
A1
E
D0
D2
D1
D3
A0
A1
E
1
1
1
1
Input:
1000D8 = 1

## Slide 55: Constructing 4x16 Decoder using 2x4 Decoders Only
A0
A1
A2
A3
D0 = 1
D2
D4 = 1
D6
D1
D3
D5
D7
D8 = 1
D10
D12 = 1
D14
D9
D11
D13
D15
D0
D2
D1
D3
D0
D2
D1
D3
A0
A1
E
A0
A1
E
D0
D2
D1
D3
A0
A1
E
D0
D2
D1
D3
A0
A1
E
1
1
1
1
Input:
1000D8 = 1
0
0
0
0
0
0
0
0
0
0

## Slide 56: Constructing 4x16 Decoder using 2x4 Decoders Only
A0
A1
A2
A3
D0
D2=1
D4
D6=1
D1
D3
D5
D7
D8
D10=1
D12
D14=1
D9
D11
D13
D15
D0
D2
D1
D3
D0
D2
D1
D3
A0
A1
E
A0
A1
E
D0
D2
D1
D3
A0
A1
E
D0
D2
D1
D3
A0
A1
E
1
1
1
1
Input:
1010D10 = 1
0
1
0
1
0
1
0
1
0
1

## Slide 57: Constructing 4x16 Decoder using 2x4 Decoders Only
A0
A1
A2
A3
D0
D2
D4
D6
D1
D3
D5
D7
D8
D10
D12
D14
D9
D11
D13
D15
D0
D2
D1
D3
D0
D2
D1
D3
A0
A1
E
A0
A1
E
D0
D2
D1
D3
A0
A1
E
D0
D2
D1
D3
A0
A1
E
D0
D2
D1
A0
A1
D3
2x4
2x4
2x4
2x4
2x4
Decoder
Input:
1000D8 = 1
0
0
0
1

## Slide 58: Constructing 4x16 Decoder using 2x4 Decoders Only
A0
A1
A2
A3
D0 = 0
D2 = 0
D4 = 0
D6 = 0
D1 = 0
D3 = 0
D5 = 0
D7 = 0
D8 = 1
D10 = 0
D12 = 0
D14 = 0
D9 = 0
D11 = 0
D13 = 0
D15 = 0
D0
D2
D1
D3
D0
D2
D1
D3
A0
A1
E
A0
A1
E
D0
D2
D1
D3
A0
A1
E
D0
D2
D1
D3
A0
A1
E
D0
D2
D1
A0
A1
D3
2x4
2x4
2x4
2x4
2x4
Decoder
Input:
1000D8 = 1
0
0
0
1
0
0
1
0
0
0

## Slide 59: Constructing 4x16 Decoder using 2x4 Decoders Only
A0
A1
A2
A3
D0 = 0
D2 = 0
D4 = 0
D6 = 0
D1 = 0
D3 = 0
D5 = 0
D7 = 0
D8 = 0
D10 = 0
D12 = 0
D14 = 0
D9 = 0
D11 = 0
D13 = 1
D15 = 0
D0
D2
D1
D3
D0
D2
D1
D3
A0
A1
E
A0
A1
E
D0
D2
D1
D3
A0
A1
E
D2
D1
D3
A0
A1
E
D0
D2
D1
A0
A1
D3
2x4
2x4
2x4
2x4
2x4
Decoder
Input:
1101D13 = 1
1
0
1
1
0
0
0
1
1
0
D0

## Slide 60: Constructing 3x8 Decoder using two 2x4 Decoders
A2 | A1 | A0 | Output 1 at
0 | 0 | 0 | D0
0 | 0 | 1 | D1
0 | 1 | 0 | D2
0 | 1 | 1 | D3
1 | 0 | 0 | D4
1 | 0 | 1 | D5
1 | 1 | 0 | D6
1 | 1 | 1 | D7

## Slide 61: Constructing 5x32 Decoder using four 3x8 and one 2x4 Decoder(s) Only
5x32
Decoder
A0
A1
A2
A3
D0
D2
D4
D6
D1
D3
D5
D7
D8
D10
.
.
D30
D9
.
D31
A4

## Slide 62: Constructing 5x32 Decoder using four 3x8 and one 2x4 Decoder(s) Only
A3
A4
D7 … D0
A0
A1
E
A0
A1
E
A0
A1
E
A0
A1
E
D0
D2
D1
A0
A1
D3
3x8
3x8
3x8
3x8
2x4
Decoder
D15 … D8
D23… D16
D31…D24
A2
A2
A2
A2
A2 - A0
A2 - A0
A2 - A0
A2 - A0
A0
A1
A2

## Slide 63: Constructing 5x32 Decoder using four 3x8 and one 2x4 Decoder(s) Only
A3
A4
D7 - D0
A0
A1
E
A0
A1
E
A0
A1
E
A0
A1
E
D0
D2
D1
A0
A1
D3
3x8
3x8
3x8
3x8
2x4
Decoder
D15 - D8
D23 - D16
D31 - D24
A2
A2
A2
A2
A2 - A0
A2 - A0
A2 - A0
A2 - A0
Input:
10110D22 = 1
A0
A1
A2
0
1
1
0
1

## Slide 64: Constructing 5x32 Decoder using four 3x8 and one 2x4 Decoder(s) Only
A3
A4
D7 - D0
A0
A1
E
A0
A1
E
A0
A1
E
A0
A1
E
D0
D2
D1
A0
A1
D3
3x8
3x8
3x8
3x8
2x4
Decoder
D15 - D8
D23 - D16
D31 - D24
A2
A2
A2
A2
A2 - A0
A2 - A0
A2 - A0
A2 - A0
Input:
10110D22 = 1
A0
A1
A2
0
1
1
0
1
0
0
1
0
110
D22 = 1

## Slide 65: Constructing 5x32 Decoder using four 3x8 and one 2x4 Decoder(s) Only
A3
A4
D7 - D0
A0
A1
E
A0
A1
E
A0
A1
E
A0
A1
E
D0
D2
D1
A0
A1
D3
3x8
3x8
3x8
3x8
2x4
Decoder
D15 - D8
D23 - D16
D31 - D24
A2
A2
A2
A2
A2 - A0
A2 - A0
A2 - A0
A2 - A0
Input:
10110What will be the output now?
A0
A1
A2
0
1
1
0
1
0
0
1
0
110
D22 = 1
E
E
E = 0