## Slide 1: Multiplexer
Reference: Chapter 3
Moris Mano 4th Edition

## Slide 2: Multiplexer (MUX/Data Selector)
Used for Selection
Takes 2n information inputs
Sends only one input to output line always
Based on n selection input
m - to - 1
MUX
(m = 2n)
I0
S0
Y
I1
.
.
Im-1
Sn-1
…

## Slide 3: 2-to-1 Multiplexer
Truth table for 2x1 MUX
2×1
MUX
Y
I0
I1
S
S | Y
0 | I0
1 | I1
Condensed Truth Table

## Slide 4: 2-to-1 Multiplexer
D0
D1

## Slide 5: 2-to-1 Multiplexer
D0 = 1
D1 = 0
0
0
I0
X.1 = X
X.0 = 0
= I0
Dj . Ij
If Ij = 0  0 Passed forward
If Ij = 1  Ij Passed forward

## Slide 6: 2-to-1 Multiplexer
D0 = 0
D1 = 1
1
0
I1
= I1

## Slide 7: 2-to-1 Multiplexer
S’
S
S’I0
SI1
Derive Equation from Circuit:
Y = S’I0 + SI1
S’I0 + SI1

## Slide 8: 4-to-1 Multiplexer
4×1
MUX
Y
I0
I1
S1
I2
I3
S0
Condensed Truth Table
MUX Block
4 = 22
2 Selection Inputs

## Slide 9: 4-to-1 Multiplexer
Condensed Truth Table
nx2^n Decoder

## Slide 10: 4-to-1 Multiplexer
Condensed Truth Table
nx2^n Decoder
1
0

## Slide 11: 4-to-1 Multiplexer
Condensed Truth Table
nx2^n Decoder
1
0
1
0
0
0

## Slide 12: 4-to-1 Multiplexer
Condensed Truth Table
nx2^n Decoder
1
0
1
0
0
0
I2
0
0
0

## Slide 13: 4-to-1 Multiplexer
Condensed Truth Table
nx2^n Decoder
1
0
1
0
0
0
I2
0
0
0
I2

## Slide 14: 4-to-1 Multiplexer
Condensed Truth Table
nx2^n Decoder
0
0

## Slide 15: 4-to-1 Multiplexer
Condensed Truth Table
nx2^n Decoder
0
0
0
1
0
0

## Slide 16: 4-to-1 Multiplexer
Condensed Truth Table
nx2^n Decoder
0
0
0
1
0
0
0
I0
0
0

## Slide 17: 4-to-1 Multiplexer
Condensed Truth Table
nx2^n Decoder
0
0
0
1
0
0
0
I0
0
0
I0

## Slide 18: 4-to-1 Multiplexer
Condensed Truth Table
Write Equation for this MUX (output Y)

## Slide 19: 4-to-1 Multiplexer
Condensed Truth Table

## Slide 20: 4-to-1 Multiplexer
Condensed Truth Table
Y = m0I0 + m1I1 + m2I2 + m3I3

## Slide 21: Multiplexer Functionality
Forward Information Ix to output Line Y where (x)10 = (Sn-1Sn-2…S1S0)2

## Slide 22: 8x1 MUX
Equation and Circuit
Do yourself

## Slide 23: 64-to-1 Multiplexer
2^6 = 64

## Slide 24: 2-to-1 Quadruple Multiplexer
  Quadruple  Information size = 4-bits
  Takes two 4-bit numbers e.g.
    A = 1011
    B = 1101
  Sends one of the numbers to output (Total 4 output lines, 1 line per bit)
No of selection doesn’t not depends on bits it stills depends on no of ips. By ALI
S | Y
0 | Select A
1 | Select B
2x1
Quad
MUX
A
B
Y
S

## Slide 25: 2-to-1 Quadruple Multiplexer
2x1
Quad
MUX
A
B
Y
S

## Slide 26: 2-to-1 Quadruple Multiplexer
2x1
Quad
MUX
A
B
Y
S
E = 0
1

## Slide 27: 2-to-1 Quadruple Multiplexer
2x1
Quad
MUX
A
B
Y
S
S = 0
E = 0
1
S = 1
S = 1
S = 1
S = 1
S = 0
S = 0
S = 0

## Slide 28: 2-to-1 Quadruple Multiplexer
2x1
Quad
MUX
A
B
Y
S
S = 0
E = 0
1
S = 1
S = 1
S = 1
S = 1
S = 0
S = 0
S = 0
A1
0
0
0
0
A2
A3
A4

## Slide 29: 2-to-1 Quadruple Multiplexer
2x1
Quad
MUX
A
B
Y
S
S = 0
E = 0
1
S = 1
S = 1
S = 1
S = 1
S = 0
S = 0
S = 0
A1
0
0
0
0
A2
A3
A4
0
0
0
0
Yi = Ai

## Slide 30: 4-to-1 Quad Multiplexer
4x1
Quad
MUX
A
B
Y
S1
C
D
S0

## Slide 31: 4-to-1 Quad Multiplexer
S0
S1
Total Information
= 4 (e.g. 4 Numbers)
Size of Information
= 4 (Each no. of 4 bits)

## Slide 32: 4x1 Dual Multiplexer
Total Channel (of Information) = 4
Dual means each Number of 2-bits
For example,
  A = 10, B = 11, C = 01 and D = 00
Sends one of the numbers to output according to the selection input (Total 2 output lines required)
Do yourself

## Slide 33: Size of MUX
Always sends 1 out of 2^n information
Information Size ……. MUX Output Size (Output wires)
  1 …….. 1
  4 …….. 4
  2 …….. 2
  x …….. X
  What will be the configuration of MUX if we need to select only 1 out of 16 characters ( Suppose, 1 character = 8 bits ). Can you design it using single bit 16x1 MUX(s)?

## Slide 34: Implementing Boolean Function using MUX
X | Y | Z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Step 1: Truth Table of Function

## Slide 35: Implementing Boolean Function using MUX
Step 2: Give first n-1 function variables as Selection Inputs to Multiplexer. Give Ij (Information
bits) according to the relationship found
X | Y | Z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
4×1
MUX
F
I0
I1
S1
I2
I3
S0
Y
X
Least Significant Bit
Total Vars = n
Selection Inputs
= n-1
2(n-1)x1 MUX

## Slide 36: Implementing Boolean Function using MUX
Step 2: Give first n-1 function variables as Selection Inputs to Multiplexer. Give Ij (Information
bits) according to the relationship found
X | Y | Z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
4×1
MUX
F
I0
I1
S1
I2
I3
S0
Y
X
Least Significant Bit
Total Vars = n
Selection Inputs
= n-1
2(n-1)x1 MUX
?
?
?
?

## Slide 37: Implementing Boolean Function using MUX
Step 2: Give first n-1 function variables as Selection Inputs to Multiplexer. Give Ij (Information
bits) according to the relationship found
X | Y | Z | F | 
0 | 0 | 0 | 0 | F = Z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 
4×1
MUX
F
I0
I1
S1
I2
I3
S0
Y
X
Z
Total Vars = n
Selection Inputs
= n-1
2(n-1)x1 MUX
Check behavior of F on
(XY) = (00)

## Slide 38: Implementing Boolean Function using MUX
Step 2: Give first n-1 function variables as Selection Inputs to Multiplexer. Give Ij (Information
bits) according to the relationship found
X | Y | Z | F | 
0 | 0 | 0 | 0 | F = Z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = Z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 
4×1
MUX
F
I0
I1
S1
I2
I3
S0
Y
X
Z
Total Vars = n
Selection Inputs
= n-1
2(n-1)x1 MUX
Check behavior of F on
(XY) = (01)
Z’

## Slide 39: Implementing Boolean Function using MUX
Step 2: Give first n-1 function variables as Selection Inputs to Multiplexer. Give Ij (Information
bits) according to the relationship found
X | Y | Z | F | 
0 | 0 | 0 | 0 | F = Z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = Z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 
4×1
MUX
F
I0
I1
S1
I2
I3
S0
Y
X
Z
Total Vars = n
Selection Inputs
= n-1
2(n-1)x1 MUX
Check behavior of F on
(XY) = (10)
Z’
0

## Slide 40: Implementing Boolean Function using MUX
Step 2: Give first n-1 function variables as Selection Inputs to Multiplexer. Give Ij (Information
bits) according to the relationship found
X | Y | Z | F | 
0 | 0 | 0 | 0 | F = Z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = Z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F=1
1 | 1 | 1 | 1 | 
4×1
MUX
F
I0
I1
S1
I2
I3
S0
Y
X
Z
Total Vars = n
Selection Inputs
= n-1
2(n-1)x1 MUX
Check behavior of F on
(XY) = (10)
Z’
0
1

## Slide 41: Implementing Boolean Function using MUX
Step 2: Give first n-1 function variables as Selection Inputs to Multiplexer. Give Ij (Information
bits) according to the relationship found
X | Y | Z | F | 
0 | 0 | 0 | 0 | F = Z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = Z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F=1
1 | 1 | 1 | 1 | 
4×1
MUX
F
I0
I1
S1
I2
I3
S0
Y
X
Z
Z’
0
1
Test Circuit on different inputs
Total Vars = n
Selection Inputs
= n-1
2(n-1)x1 MUX

## Slide 42: Implementing Boolean Function using MUX
Step 3: Give first n-1 function variables as Selection Inputs to Multiplexer. Give Ij (Information
bits) according to the relationship found
X | Y | Z | F | 
0 | 0 | 0 | 0 | F = Z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = Z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F=1
1 | 1 | 1 | 1 | 
4×1
MUX
F
I0
I1
S1
I2
I3
S0
MUX Implementation
Y
X
Z
Z’
0
1
Input = (XYZ) = 101
1
0

## Slide 43: Implementing Boolean Function using MUX
Step 3: Give first n-1 function variables as Selection Inputs to Multiplexer. Give Ij (Information
bits) according to the relationship found
4×1
MUX
F
I0
I1
S1
I2
I3
S0
MUX Implementation
Y
X
Z
Z’
0
1
Input = (XYZ) = 101
1
0
= I2= 0
X | Y | Z | F | 
0 | 0 | 0 | 0 | F = Z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = Z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F=1
1 | 1 | 1 | 1 | 

## Slide 44: Implementing Boolean Function using MUX
Step 3: Give first n-1 function variables as Selection Inputs to Multiplexer. Give Ij (Information
bits) according to the relationship found
X | Y | Z | F | 
0 | 0 | 0 | 0 | F = Z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = Z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F=1
1 | 1 | 1 | 1 | 
4×1
MUX
F
I0
I1
S1
I2
I3
S0
MUX Implementation
Y
X
Z
Z’
0
1
Input = (XYZ) = 001
0
0
= I0= Z
= 1

## Slide 45: Implementing Boolean Function using MUX
F(A,B,C,D) = ∑m(1,3,4,11,12,13,14,15)
Total Variables = n = 4
Selection Variables = n-1 = 3
2^3 = 8  8x1 MUX Required

## Slide 46: Implementing Boolean Function using MUX
F(A,B,C,D) = ∑m(1,3,4,11,12,13,14,15)
MUX Implementation of four variable function

## Slide 47: Implementing Boolean Function using MUX
F(A,B,C,D) = ∑m(1,3,4,11,12,13,14,15)
Can you implement this function using 4x1 MUX having A and B as Selection Inputs and
C and D as Data Inputs?

## Slide 48: Multiplexer Implementation of 1 Bit Adder
2 Output bits  Dual MUX Required
Total input variables = n = 3
Selection inputs = n-1 = 2
Required MUX Size:
(2^2) 4 x 1 Dual MUX

## Slide 49: Multiplexer Implementation of 1 Bit Adder
Ix,y means Information no. x and bit y

## Slide 50: Multiplexer Implementation of 1 Bit Adder
Ix,y means Information no. x and bit y
00

## Slide 51: Multiplexer Implementation of 1 Bit Adder
Ix,y means Information no. x and bit y
01

## Slide 52: Multiplexer Implementation of 1 Bit Adder
Ix,y means Information no. x and bit y
10

## Slide 53: Multiplexer Implementation of 1 Bit Adder
Ix,y means Information no. x and bit y
11

## Slide 54: Implementing Function using MUX
4×1
MUX
F(A,B,C,D)
I0
I1
S1
I2
I3
S0
B
A
1
D
Determine Function Implemented by following MUX
C
D
C
D
A | B | C | D | F
0 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 
0 | 0 | 1 | 0 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | 
0 | 1 | 0 | 1 | 
0 | 1 | 1 | 0 | 
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | 
1 | 0 | 0 | 1 | 
1 | 0 | 1 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 
1 | 1 | 1 | 1 | 

## Slide 55: Implementing Function using MUX
4×1
MUX
F(A,B,C,D)
I0
I1
S1
I2
I3
S0
B
A
1
D
Determine Function Implemented by following MUX
C
D
C
D
A | B | C | D | F
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1

## Slide 56: DeMultiplexer

## Slide 57: Demultiplexer
Inverse of Multiplexer
Receives information from single line
Transmits it to one of 2^n output lines
Based on n Selection Inputs
Circuit is same as 2x4 Line Decoder with enable input
1-to-4 Line Demultiplexer
Data Input

## Slide 58: Demultiplexer
For example,
(S1S0) = (10)2
1-to-4 Line Demultiplexer
1
0
Data Input
1
0
0
0

## Slide 59: Demultiplexer
For example,
(S1S0) = (10)2
1-to-4 Line Demultiplexer
1
0
Data Input
1
0
0
0
Data Input
0
0
0

## Slide 60: 1-to-m Line Demultiplexer
1×2n
Demultiplexer
(m = 2n)
S1
D2
D0
D1
S0
Sn-1
.
.
.
Data Input
Dm-2
Dm-1
.
.
.

## Slide 61: Making Larger Size MUX using Smaller MUX(s)

## Slide 62: Dual 2x1 MUX Using single 2x1 MUX(s) Only
2x1
MUX
2x1
MUX
A0
B0
A1
B1
Y0
Y1
Selection Input S | Y
0 | A
1 | B
S
S

## Slide 63: Dual 2x1 MUX Using single 2x1 MUX(s) Only
2x1
MUX
2x1
MUX
A0
B0
A1
B1
Y0
Y1
Selection Input S | Y
0 | A
1 | B
S
S
1
1

## Slide 64: Dual 2x1 MUX Using single 2x1 MUX(s) Only
2x1
MUX
2x1
MUX
A0
B0
A1
B1
Y0
Y1
Selection Input S | Y
0 | A
1 | B
S
S
1
1
= B0
= B1

## Slide 65: Dual 2x1 MUX Using single 2x1 MUX(s) Only
2x1
MUX
2x1
MUX
A0
B0
A1
B1
Y0
Y1
Selection Input S | Y
0 | A
1 | B
S
S
0
0
= A0
= A1

## Slide 66: Implement 17x1 MUX using 4x1 MUX(s) and 2x1 MUX(s)
17x1
MUX
I16-I0
Y
S0
S1
S2
S3
S4

## Slide 67: Implement 17x1 MUX using 4x1 MUX(s) and 2x1 MUX(s) Condensed Truth Table
Selection Input | Output | Selection Input | Output
S4S3S2S1S0 | Y | S4S3S2S1S0 | Y
00000 | I0 | 01000 | I8
00001 | I1 | 01001 | I9
00010 | I2 | 01010 | I10
00011 | I3 | 01011 | I11
00100 | I4 | 01100 | I12
00101 | I5 | 01101 | I13
00110 | I6 | 01110 | I14
00111 | I7 | 01111 | I15
 |  | 10000 | I16
 |  | Rest of Combinations | Don’t Care

## Slide 68: 17x1 MUX using 4x1 and 2x1 MUX(s)
4x1
MUX
I3-I0
Y
S0
S1
S2
S3
S4
4x1
MUX
I7-I4
S0
S1
4x1
MUX
I11-I8
S0
S1
4x1
MUX
I15-I12
S0
S1
4x1
MUX
I0
I1
I2
I3
2x1
MUX
I16

## Slide 69: 17x1 MUX using 4x1 and 2x1 MUX(s)
4x1
MUX
I3-I0
Y
S0
S1
S2
S3
S4
4x1
MUX
I7-I4
S0
S1
4x1
MUX
I11-I8
S0
S1
4x1
MUX
I15-I12
S0
S1
4x1
MUX
I0
I1
I2
I3
2x1
MUX
I16
Selection Input = 01100
Expected Result:
Y = I12

## Slide 70: 17x1 MUX using 4x1 and 2x1 MUX(s)
4x1
MUX
I3-I0
Y
S0
S1
S2
S3
S4
4x1
MUX
I7-I4
S0
S1
4x1
MUX
I11-I8
S0
S1
4x1
MUX
I15-I12
S0
S1
4x1
MUX
I0
I1
I2
I3
2x1
MUX
I16
Selection Input = 01100
Expected Result:
Y = I12
0
0
0
0
0
0
0
0

## Slide 71: 17x1 MUX using 4x1 and 2x1 MUX(s)
4x1
MUX
I3-I0
Y
S0
S1
S2
S3
S4
4x1
MUX
I7-I4
S0
S1
4x1
MUX
I11-I8
S0
S1
4x1
MUX
I15-I12
S0
S1
4x1
MUX
I0
I1
I2
I3
2x1
MUX
I16
Selection Input = 01100
Expected Result:
Y = I12
0
0
0
0
0
0
0
0
I0
I4
I8
I12

## Slide 72: 17x1 MUX using 4x1 and 2x1 MUX(s)
4x1
MUX
I3-I0
Y
S0
S1
S2
S3
S4
4x1
MUX
I7-I4
S0
S1
4x1
MUX
I11-I8
S0
S1
4x1
MUX
I15-I12
S0
S1
4x1
MUX
I0
I1
I2
I3
2x1
MUX
I16
Selection Input = 01100
Expected Result:
Y = I12
0
0
0
0
0
0
0
0
I0
I4
I8
I12
1
1
I12

## Slide 73: 17x1 MUX using 4x1 and 2x1 MUX(s)
4x1
MUX
I3-I0
Y
S0
S1
S2
S3
S4
4x1
MUX
I7-I4
S0
S1
4x1
MUX
I11-I8
S0
S1
4x1
MUX
I15-I12
S0
S1
4x1
MUX
I0
I1
I2
I3
2x1
MUX
I16
Selection Input = 01100
Expected Result:
Y = I12
0
0
0
0
0
0
0
0
I0
I4
I8
I12
1
1
I12
0
I12

## Slide 74: 17x1 MUX using 4x1 and 2x1 MUX(s)
4x1
MUX
I3-I0
Y
S0
S1
S2
S3
S4
4x1
MUX
I7-I4
S0
S1
4x1
MUX
I11-I8
S0
S1
4x1
MUX
I15-I12
S0
S1
4x1
MUX
I0
I1
I2
I3
2x1
MUX
I16
Selection Input = 10000
Expected Result:
Y = I16

## Slide 75: 17x1 MUX using 4x1 and 2x1 MUX(s)
4x1
MUX
I3-I0
Y
S0
S1
S2
S3
S4
4x1
MUX
I7-I4
S0
S1
4x1
MUX
I11-I8
S0
S1
4x1
MUX
I15-I12
S0
S1
4x1
MUX
I0
I1
I2
I3
2x1
MUX
I16
0
0
0
0
0
0
0
0
Selection Input = 10000
Expected Result:
Y = I16

## Slide 76: 17x1 MUX using 4x1 and 2x1 MUX(s)
4x1
MUX
I3-I0
Y
S0
S1
S2
S3
S4
4x1
MUX
I7-I4
S0
S1
4x1
MUX
I11-I8
S0
S1
4x1
MUX
I15-I12
S0
S1
4x1
MUX
I0
I1
I2
I3
2x1
MUX
I16
0
0
0
0
0
0
0
0
I0
I4
I8
I12
Selection Input = 10000
Expected Result:
Y = I16

## Slide 77: 17x1 MUX using 4x1 and 2x1 MUX(s)
4x1
MUX
I3-I0
Y
S0
S1
S2
S3
S4
4x1
MUX
I7-I4
S0
S1
4x1
MUX
I11-I8
S0
S1
4x1
MUX
I15-I12
S0
S1
4x1
MUX
I0
I1
I2
I3
2x1
MUX
I16
0
0
0
0
0
0
0
0
I0
I4
I8
I12
0
0
I0
Selection Input = 10000
Expected Result:
Y = I16

## Slide 78: 17x1 MUX using 4x1 and 2x1 MUX(s)
4x1
MUX
I3-I0
Y
S0
S1
S2
S3
S4
4x1
MUX
I7-I4
S0
S1
4x1
MUX
I11-I8
S0
S1
4x1
MUX
I15-I12
S0
S1
4x1
MUX
I0
I1
I2
I3
2x1
MUX
I16
Selection Input = 01100
Expected Result:
Y = I12
0
0
0
0
0
0
0
0
I0
I4
I8
I12
1
1
I0
1
I16